## Slide 1
HISTORY · RECAP
The Greek temple
Its parts, the three orders and three temples of Athens
Notes: A Greek temple is a god's house. This deck walks through how one is built, from the floor plan to the roof, and how to spot a Doric, an Ionic and a Corinthian column.

## Slide 2
A PUZZLE AT THE BACK
Why is there a room behind
the cella that has no door
into it?
Notes: It is the opisthodomos, the twin of the pronaos. It has no door to the cella because it exists for looks: a temple ringed with columns is seen from every side, so the front is repeated at the back. In the Parthenon, from 433 BC, the western room held the city's public money.

## Slide 3
FROM THE CELLA TO THE PARTHENON
01
What the temple was for
02
Floor plan and elevation
03
Telling the orders apart
04
Parthenon, Erechtheion, Athena Nike

## Slide 4
WALKING IN FROM THE FRONT
Pronaos
Porch with two columns between the walls
Naos
The cella holding the god's statue
Opisthodomos
Back room, no door to the cella
Notes: The pronaos is made by the side walls extended forward, the antae, with two columns between them, and a door leads from it into the naos. The opisthodomos lies behind. Around all four sides runs the peristasis, normally one row of columns, which sheltered visitors and gave room for processions.

## Slide 5
BOTTOM
Crepidoma
3 steps
The top one is the stylobate
MIDDLE
Columns
24 flutes
Doric has 18 to 20
TOP
Entablature
3 parts
Architrave, frieze, cornice
Notes: Seen from the side, the temple always splits into three zones. The underground foundation is the stereobate, and above it comes the crepidoma of three steps. The architrave rests on the capitals and carries what is above it, the frieze is mainly decoration, and the cornice projects to protect what lies beneath. Ionic and Corinthian columns normally have 24 flutes, Doric ones 18 to 20.

## Slide 6
WHAT TO LOOK AT ON A PHOTO
Doric
Shaft with no base
Echinus and square abacus, frieze of triglyphs and metopes.
Ionic
Base and two scrolls
Plain or figured frieze, sometimes with dentils.
Corinthian
Capital of acanthus
Scrolls at the corners, Doric or Ionic entablature above.
Notes: Treccani defines an order as a series of columns together with the entablature above them. According to Vitruvius, the Corinthian never had an entablature of its own and borrows the Doric or the Ionic one. A Doric column stands directly on the stylobate, while Ionic and Corinthian columns have a base.

## Slide 7
MYTH
Greek temples were colourful.
Vivid reds and blues stood out against the white of the stone or plaster. On a Doric frieze the triglyphs were blue and the metopes red, in alternation.
Notes: The palette was white, blue and red, with some black. Colour sat chiefly on parts that bear nothing: columns and architrave of good limestone or marble were left unpainted, or covered with white stucco.

## Slide 8
THE PARTHENON, DORIC AND PERIPTERAL: A COLONNADE ON ALL FOUR SIDES
8
columns: Across the front and back
17
columns: Along each side
447-438
BC, years of construction: Pediments finished in 432 BC
Notes: The design is credited to the architects Iktinos and Kallikrates, with overall direction and the sculptural programme entrusted to Pheidias. The cella held the gold and ivory statue of Athena, a work of Pheidias. In 1687, during the Venetian siege of the Acropolis, an explosion of the gunpowder the Turks kept in the building brought down large parts of it.

## Slide 9
YOUR TURN
What is unique about the Parthenon among Doric temples?
A A cella split into two aisles by a row of columns
B A roof of terracotta tiles painted red
C A continuous Ionic frieze running around the cella
Notes: Around the outside of the cella runs an Ionic frieze showing the Panathenaic procession, the great festival of Athens. A second question for the class: which part of the entablature is mainly decoration?

## Slide 10
TIME TO REVIEW
Clear in 30 seconds.
Yours in 10 minutes.
Quiz, flashcards and concept map on the Greek temple recaplica.com/en/history/greek-temple/
Sources: Treccani · Acropolis Restoration Service · Vitruvius · Wikipedia
Notes: The sources are listed at the bottom of the Recap page.