## Slide 1
SCIENCE · RECAP
How Beer Is Made
From barley to glass, step by step
Notes: Beer comes from four ingredients, water, malted barley, hops and yeast, combined through four main steps.

## Slide 2
THE FIRST MYTH
Can raw barley make beer?
Notes: No, it takes malted barley, barley that has been germinated and then dried. Raw grain lacks the enzymes needed to turn starch into fermentable sugar.

## Slide 3
FOUR STAGES
01
Malting
02
Mashing
03
Fermentation
04
History and rules

## Slide 4
MALTING IN THREE STEPS
Steeping
Two to three days in water
Germination
Six to ten days, enzymes appear
Kilning
Heat decides the malt's color
Notes: During germination the barley produces the enzymes mashing will need later, then kilning stops germination, and the temperature reached decides whether the malt turns out pale or roasted.

## Slide 5
WHAT HAPPENS INSIDE THE WORT
30%
typical ceiling on hop utilization in a brewery: alpha-acid yield during boiling rarely goes above this
18%
alpha acids in the bitterest hop varieties: against 2.5% in the most aromatic ones
Notes: The hops' alpha acids, held in the lupulin resin, are almost insoluble in cold water, only boiling isomerizes them into soluble, bitter compounds.

## Slide 6
YEAST MAKES THE CALL
Ale
YEAST
Saccharomyces cerevisiae
TEMPERATURE
16-26°C
Lager
YEAST
Saccharomyces pastorianus
TEMPERATURE
9-14°C
The yeast strain decides the style
Notes: Ales ferment on the surface with esters and phenols, fruity or spicy notes, lagers ferment at the bottom, colder, with a cleaner taste, then mature for weeks near freezing.

## Slide 7
STAGE 1
Enterobacteriaceae
3-40 days
the first wild microbes
STAGE 2
Saccharomyces
3-4 weeks
yeast dominates through month 3-4
STAGE 3
Pediococcus
3-4 months
lactic souring begins
Notes: In lambic the wort cools overnight in open vessels, the coolship, and gets colonized by microorganisms from the air and the barrels, with no selected yeast added, in a process that lasts one to three years.

## Slide 8
MYTH BUSTED
The 1516 decree never mentioned yeast
yeast hadn't been discovered yet, and the name Reinheitsgebot was only coined in 1918.
Notes: The 1516 text limited ingredients to barley, hops and water; yeast entered the law only after its scientific discovery, well over a century later.

## Slide 9
ON THE BOARD
What makes lambic fermentation special?
A It uses a selected yeast at high temperature
B Wild microorganisms from the air and the barrels trigger it
C It's done in a few hours inside sealed tanks
Notes: Answer, the second option, the wort is colonized by wild microorganisms with no added cultures, in a process lasting one to three years. Second question for the class, what other fermented drink do you know that skips an added yeast?

## Slide 10
CHEERS
Clear in 30 seconds.
Yours in 10 minutes.
Read the full Recap on Recaplica recaplica.com/en/science/how-beer-is-made/
Sources: American Homebrewers Association · Oxford Companion to Beer · BJCP · PLoS ONE
Notes: Four stages, malting, mashing, boiling and fermentation, decide together what kind of beer ends up in the glass.