## Slide 1
SCIENCE · RECAP
Nuclear Fission and Fusion
Two ways to release the energy locked in the atomic nucleus
Notes: Today we look inside the atomic nucleus, at the two ways it releases energy: by splitting or by joining.

## Slide 2
ONE HEAVY NUCLEUS, ONE LIGHT NUCLEUS
Do a nuclear plant and the
Sun run on the same
process?
Notes: No. A nuclear plant splits heavy nuclei, that's fission. The Sun joins light nuclei, that's fusion. Different reactions, both releasing energy from the atomic nucleus.

## Slide 3
FROM A HEAVY NUCLEUS TO A LIGHT ONE
01
How fission works
02
How fusion works
03
Who is testing fusion
04
The two processes, compared
Notes: We'll cover fission first, then fusion, then three ongoing experiments, and finally a direct comparison.

## Slide 4
01
CHAPTER
Fission
A heavy nucleus splits in two

## Slide 5
JUST ONE NEUTRON, OUT OF 2.45, KEEPS IT GOING
The heat
about 85% of the energy becomes heat
The impact
a neutron strikes a uranium-235 nucleus
The split
the nucleus breaks into two smaller nuclei
The release
energy and an average of 2.45 new neutrons come free
Notes: Each fission releases an average of 2.45 neutrons: only one needs to trigger another fission to sustain the chain reaction, the rest are lost or absorbed.

## Slide 6
200 MEV PER FISSION
200
MeV per uranium-235 fission: energy released by a single nucleus struck by a neutron
2.45
neutrons released on average: can trigger further fissions in the chain reaction
82
TJ of energy from one kilogram of fuel: the energy equivalent of fissioning one kilogram of uranium-235
Notes: These are the baseline physics figures for fission, according to the World Nuclear Association.

## Slide 7
02
CHAPTER
Fusion
Two light nuclei join into one

## Slide 8
THE PLASMA CLIMBS TO TENS OF MILLIONS OF DEGREES
ITER
project target, 150 million degrees
Heating
the fuel, hydrogen isotopes, is heated to extreme temperatures
Confinement
a magnetic field holds the rarefied plasma together, inside a tokamak
The merge
a deuterium and a tritium nucleus join and release energy
Notes: Triggering fusion on Earth takes heating the fuel to roughly 50 million degrees; ITER targets 150 million degrees, ten times the Sun's core.

## Slide 9
17.6 MEV PER FUSION
17.6
MeV per deuterium-tritium fusion: less than the 200 MeV of a single uranium-235 fission
50
million degrees to trigger fusion: the order of magnitude needed for fuel on Earth
1951
year the tokamak was designed: devised by Soviet physicists Andrei Sakharov and Igor Tamm
Notes: The tokamak remains the most common configuration among experimental fusion reactors.

## Slide 10
FROM 2022 TO 2026, THREE FUSION MILESTONES
NIF
the U.S. laser laboratory
on December 5, 2022, passed scientific energy breakeven for the first time in a laboratory, 3.15 megajoules produced against 2.05 delivered
EAST
the Chinese tokamak
in January 2025, sustained a plasma for 1,066 seconds, more than double the 2023 record
ITER
the tokamak under construction in France
as of October 2026, is still being assembled, targeting 500 MW from 50 MW of input
Notes: Three different experiments, three ways of measuring progress in fusion research.

## Slide 11
SAME NUCLEUS, TWO REACTIONS
Fission
INSIDE THE NUCLEUS
a heavy nucleus, such as uranium-235, splits in two
PER EVENT
releases about 200 MeV of energy
Fusion
INSIDE THE NUCLEUS
two light hydrogen nuclei join into one
PER EVENT
releases 17.6 MeV of energy
Fission wins per single event, fusion wins per kilogram of fuel.
Notes: The direct comparison: fission releases more energy at every single event, but fusion releases more per unit of fuel mass.

## Slide 12
WHERE THE RESEARCH STANDS, AS OF OCTOBER 2026
Fission already runs power plants. Fusion is still a laboratory pursuit.
Fission is the process already used in today's nuclear plants, and it leaves long-lived radioactive waste. Fusion is not expected to produce that kind of waste, but as of October 2026 no fusion plant generates power at commercial scale.
Notes: This is the most concrete difference between the two reactions today: one is already deployed technology, the other is still research.

## Slide 13
TEST YOURSELF
Which releases more energy: a single uranium-235 fission or a single deuterium-tritium fusion?
A Fission, at about 200 MeV versus 17.6 MeV
B Fusion, with more energy per event
C They release the same amount of energy
Notes: The correct answer is fission: about 200 MeV against 17.6 MeV for a deuterium-tritium fusion, per single event. Follow-up for the class: what happens if you compare a full kilogram of fuel instead?

## Slide 14
NOW, THE RECAP
Clear in 30 seconds.
Yours in 10 minutes.
Read the full comparison on Recaplica recaplica.com/en/science/nuclear-fission-fusion-difference/
Sources: World Nuclear Association · ITER Organization · NRC · LLNL
Notes: The full Recap also has the quiz, flashcards, and concept map to review fission and fusion.