## Slide 1
SCIENCE · RECAP
Flood
How rain ends up pushing a river out of its banks
Notes: A flood is the temporary covering by water of land that is normally dry. These slides follow the water from the first rain to the moment the river spills out.

## Slide 2
TRY TO ANSWER
Why does a river burst its
banks?
Notes: Heavy or prolonged rain raises the discharge, the volume of water passing a point on the river in a given time. Once the banks can no longer hold it, the water spreads out and reaches homes, factories, roads and farmland.

## Slide 3
FROM THE FIRST RAIN TO THE RED ALERT
01
Overflow and flood
02
From rain to flood peak
03
Who lives in Italy's flood zones
04
Odds and warnings

## Slide 4
01
CHAPTER
Overflow and flood
Io non rischio splits the event in two

## Slide 5
IO NON RISCHIO AND THE 2007 EU DIRECTIVE
River overflow
WHAT IT IS
The river tops its banks
HOW
Spills over or breaks them
Flood
WHAT IT IS
Temporary flooding
WHERE
Land that is normally dry
The river spills out first, and the land around it floods after.
Notes: Italy's Civil Protection campaign calls the overflow the stage when the swollen river tops its banks or breaks through them. The flood is the flooding that follows. EU law also counts water arriving from the sea along the coast as a flood.

## Slide 6
02
CHAPTER
From rain to flood peak
How much water reaches the river, and how fast

## Slide 7
FROM HILLSIDE TO RIVER MOUTH
Saturated ground
Takes in less
Small basin
Peak within hours
Heavy or long rain
Falls on the whole basin
Discharge rises
Slowly on big rivers
River overflow
The banks can't hold it
Notes: The drainage basin is all the land whose surface water runs to a single mouth. Soaked ground lets little rain in, and on sealed land the water gets to the river sooner. Italy's Civil Protection Department adds that debris and vegetation in the channel hold back the current. Large rivers rise slowly; in small basins, like many in Italy, the flood peak comes a few hours after the rain.

## Slide 8
03
CHAPTER
Who lives in Italy's flood zones
ISPRA figures, data processed in 2020

## Slide 9
ITALY, ISPRA DATA PROCESSED IN 2020
6.8
million residents: In floodable areas, medium scenario
1.5
million buildings, and more: In flood-prone areas, medium scenario
34,000
cultural sites, nearly: Exposed in the medium scenario
Notes: In ISPRA data processed in 2020 and carried in its 2024 report on hydrogeological instability, the 6.8 million residents of floodable areas under the medium hazard scenario are 11.5% of Italy's population. The buildings number more than 1.5 million, 10.7% of all buildings in Italy.

## Slide 10
ARNO, NOVEMBER 1966
The Florence flood
1966
3-4 Nov
The Arno leaves its bed upstream
Florence
A wave three metres high, at 60 km/h
6 Nov
600,000 tonnes of mud in the city
1970
Law 996, civil protection framework
Notes: Ten days of heavy rain came first, and the Arno spilled out in the Casentino and the upper Valdarno before it reached Florence. With no monitoring network on the river, nobody gave warning. A plaque in Via dei Neri marks the highest water level, 4.92 metres. The Civil Protection Department reports 35 deaths in Tuscany.

## Slide 11
04
CHAPTER
Odds and warnings
Italy's map scenarios and the years between floods

## Slide 12
HIGH HAZARD
Frequent
20-50 years
Return period of the floods
MEDIUM HAZARD
Less frequent
100-200 years
Return period of the floods
LOW HAZARD
Worst case
Rare
Extreme events included
Notes: Italy's flood maps follow the three scenarios set by Legislative Decree 49 of 2010. In ISPRA's 2020 compilation, high hazard areas cover 5.4% of the country, medium hazard areas 10% and low hazard areas 14%.

## Slide 13
COMMON MYTH
A “100-year flood” comes once a century
The USGS gives it a 1% chance in every single year.
Notes: The return period is the average number of years between two floods of a given size. Over a million years, an event with a 1% yearly chance would be expected about 10,000 times, at irregular intervals.

## Slide 14
TIME TO REVIEW
According to NOAA, over how long does the rain behind a flash flood usually fall?
A Generally less than six hours
B Generally two to three days
C Generally more than a week
Notes: A flash flood comes from very heavy rain packed into a short time, usually under six hours, and the water can arrive minutes or a few hours later. A second question for the class: why do so many Italian floods arrive this fast? Because the country's basins are generally small.

## Slide 15
CONCEPT MAP, QUIZ AND FLASHCARDS ONLINE
Clear in 30 seconds.
Yours in 10 minutes.
Review floods on Recaplica recaplica.com/en/science/what-is-a-flood/
Sources: EU Directive 2007/60/EC · ISPRA · Italian Civil Protection · Io non rischio · USGS · NOAA · IPCC
Notes: The full Recap has the concept map, the quiz, the flashcards and the list of sources.