## Slide 1
TECHNOLOGY · RECAP
Axonometric Projection
Definition and how to draw it
Notes: Axonometric projection is a descriptive-geometry method for showing a three-dimensional object on a flat surface.

## Slide 2
ONE VIEW, THREE DIMENSIONS
How do you fit an object's
height, width and depth onto
one flat drawing?
Notes: The method shows all three dimensions of an object in one drawing, without needing several separate views like orthographic projection.

## Slide 3
FROM DESCRIPTIVE GEOMETRY TO THE BUILDING SITE
01
What axonometric projection is
02
The types of axonometric projection
03
How to draw it
04
Where it is used

## Slide 4
01
CHAPTER
What axonometric projection is
One view for three dimensions

## Slide 5
LINES THAT STAY PARALLEL
Axonometric projection
THE LINES
stay parallel on the page
THE MEASUREMENTS
can be read straight from the drawing
Perspective
THE LINES
converge toward a vanishing point
THE MEASUREMENTS
are not direct, the eye only estimates them
Axonometric projection reads distances straight off the drawing, not the eye.
Notes: In axonometric projection parallel lines stay parallel and the drawing does not reproduce natural vision; in perspective, lines converge and objects shrink with distance.

## Slide 6
02
CHAPTER
The types of axonometric projection
Isometric, trimetric, cavalier

## Slide 7
DIFFERENT ANGLES, DIFFERENT AXES
Isometric
120° angles, equal between the axes
The three units of measurement on the axes are identical.
Trimetric and dimetric
Unequal angles between the axes
In trimetric all three differ, in dimetric only two do.
Cavalier
The picture plane is parallel to one face of the object
That face appears in true shape, without distortion.
Notes: The three types depend on how an object's reference planes form angles with the picture plane: equal angles in isometric, unequal in trimetric and dimetric, picture plane parallel to one face in cavalier.

## Slide 8
03
CHAPTER
How to draw it
Angles, isometric scale, measurements

## Slide 9
FROM AXES TO THE ISOMETRIC SCALE
Draw the axes
120° to each other, 30° from the horizontal
Build the isometric scale
a 45° scale, projected onto a 30° line
Plot the measurements
only along the direction of the axes
Notes: In regular isometric projection the two horizontal axes are drawn tilted 30° upward; real measurements are plotted only along lines parallel to the axes, taken from the isometric scale.

## Slide 10
ISOMETRIC ANGLE AND REDUCTION FACTOR
120°
angle between each pair of axes: undefined
0.816
reduction factor for the measurements: undefined
Notes: 120° is the angle between the axes in isometric projection; 0.816, the cosine of 35°16', is the factor that reduces real measurements in true isometric projection.

## Slide 11
04
CHAPTER
Where it is used
Technical drawing and architecture

## Slide 12
REAL SCALE, NOT REDUCED
The isometric drawing taught in school is not the same as true isometric projection.
School isometric drawing plots measurements at a real 1:1 scale; true projection reduces them with a factor of about 0.816, which makes the school drawing roughly 1.23 times larger.
Notes: Isometric drawing keeps the same 120° angles as true projection but skips the reduction factor: it is larger, and simpler to produce, which is why it is the common choice in technical drawing.

## Slide 13
SAME TRUE SCALE, DIFFERENT USES
Technical drawing
Direct measurements from parallel lines
Lets you read a part's proportions without switching views.
Architecture
True-scale axes, not shortened
Axes stay at true scale, useful for communicating a project.
Exploded axonometric
Components separated along the axes
Shows how a building's parts fit together.
Notes: In architecture, axonometric projection represents buildings while keeping the axes at true scale, to communicate spaces, structure and design intent; exploded axonometric drawing separates components along the axes to show how they assemble.

## Slide 14
TRY TO ANSWER
Why is isometric projection the most common type in technical drawing?
A Because it is the easiest to draw and dimension
B Because it is the only type that shows three dimensions
C Because nothing needs to be measured
Notes: The correct answer is the first: equal 120° angles make isometric projection easier to draw and dimension than the other types. Second question for the class: what is the difference between isometric drawing and true isometric projection?

## Slide 15
NOW, THE REVIEW
Clear in 30 seconds.
Yours in 10 minutes.
Read the full Recap, with quiz and flashcards recaplica.com/en/technology/axonometric-projection/
Sources: Treccani · NPTEL · Wikipedia · illustrarch.com