## Slide 1
TECHNOLOGY · RECAP
How ATMs Work
From the card slot to the cash in your hand
Notes: An ATM is not a single box but a small cluster of specialized machines working together to recognize you, check your PIN and open the cash drawer. We will look at the parts of the machine, the encrypted journey of the PIN to the bank, the tangled history of the invention, and the most common frauds.

## Slide 2
BETWEEN THE CARD AND THE CASH
Who decides that money is
yours?
Notes: The ATM runs through three steps, never at the same time. First the reader identifies the card, then the shielded keypad accepts and encrypts the PIN, and only then does the machine ask the card-issuing bank for the green light before opening the cash drawer. The PIN you type has to match the one stored on the card's chip, if it has one, or the one held in the issuing bank's database.

## Slide 3
WHAT WE WILL COVER
01
Inside the machine
02
The PIN and the permission
03
A history with many fathers
04
The chip and the frauds

## Slide 4
01
CHAPTER
Inside the machine
Reader, shielded keypad, vault

## Slide 5
FIRST STEP
Card reader
Reads card
Chip or magnetic stripe
SECOND STEP
EPP4 keypad
Encrypts PIN
Shielded, works on the spot
LAST STEP
Vault
Releases cash
Counts and releases the notes
Notes: A CPU runs the on-screen interface and coordinates everything else. A reader, magnetic-stripe or chip, identifies the card the instant you insert it. A dedicated, shielded keypad, known in the trade as the EPP4, is built specifically to accept and encrypt the PIN you are about to type. Inside the vault, alongside the mechanism that dispenses banknotes, sit tamper sensors (magnetic, thermal, seismic or gas), dedicated locks and journaling systems that log every operation.

## Slide 6
ONE STEP AT A TIME, NEVER AT ONCE
CPU
runs the interface
ISO 8583
the bank approves
Card read
the machine knows you
PIN encrypted
never in plain text
Cash dispensed
only after the go-ahead
Notes: Once encrypted, the PIN still has to reach the card-issuing bank so it can grant, or deny, permission for the withdrawal. That exchange follows ISO 8583, an international standard that emerged in the late 1980s and was updated in 1993 and again in 2003, the same shared language behind authorization traffic for networks like Mastercard and Visa, and used by point-of-sale terminals in stores as well. The request starts at the ATM, crosses a series of intermediate networks and reaches the issuing bank's system, which approves or declines within a defined time window. Only after that green light does the vault count and release the banknotes.

## Slide 7
02
CHAPTER
The PIN and the permission
Encrypted on the spot, then the bank decides

## Slide 8
FALSE MYTH
A plain-text PIN never leaves the ATM.
The shielded EPP4 keypad encrypts it, with DES or more often Triple DES, and it passes through a dedicated device, the HSM, before it ever leaves the machine.
Notes: Many people assume that once typed, a PIN travels unencrypted over the network all the way to the bank. It actually gets encrypted immediately, inside the ATM's shielded keypad, the EPP4, using algorithms like DES or, more often in newer systems, Triple DES, and it passes through the HSM, the Hardware Security Module, a device dedicated to encryption. Traffic headed for the bank's network can also be protected with SSL. The HSM turns the typed PIN into a different, encrypted code before it leaves the machine, and protects even offline devices with an unguessable PIN-generating key.

## Slide 9
THE FATHER OF THE HSM
Mohamed Atalla
1972 – 2013
1972
Files the U.S. patent, in March
1972
Founds the Atalla Corporation
1973
The Atalla Box reaches the market
2013
250 million transactions a day
Notes: Mohamed Atalla filed the relevant U.S. patent in March 1972 and founded the Atalla Corporation, also known as Utimaco Atalla, that same year. The device, nicknamed the Atalla Box, was launched commercially in 1973, encrypting the PIN and the ATM's messages. The system consisted of a card-reader console, two customer PIN pads, an intelligent controller and a built-in electronic interface package. HSM products descended from that original invention protected 250 million card transactions a day worldwide as of 2013, and by 2014 secured the majority of ATM operations globally.

## Slide 10
THE LANGUAGE OF AUTHORIZATION
8583
the ISO standard: it emerged in the late 1980s
4
digits: flag the type of message
128
data fields: in the original specification
Notes: An ISO 8583 message breaks down, roughly, into three parts. A four-digit message type indicator, which flags whether this is an authorization request or a response. A set of data fields that can number up to 128 in the original specification, carrying card number, amount, merchant information and the authorization outcome. And a bitmap that marks which of those fields are actually present. The standard emerged in the late 1980s and was updated in 1993 and 2003, and point-of-sale terminals in stores use it too.

## Slide 11
03
CHAPTER
A history with many fathers
Three machines within weeks of each other

## Slide 12
THREE MACHINES, ALMOST AT ONCE
DACS
Barclays and De La Rue
Enfield, United Kingdom, June 27, 1967
Bankomat
Built by Sweden's Metior
Arrived nine days after Enfield
Chubb MD2
Smith Industries Chubb
A month later, and the PIN with it
Notes: The machine generally regarded as the true ancestor of the modern ATM appeared on June 27, 1967, at a Barclays branch in Enfield, north of London. The project was built by a team led by John Shepherd-Barron for the firm De La Rue, and the system was called DACS, De La Rue Automatic Cash System. It beat its rivals by a razor-thin margin, nine days ahead of the Swedish Bankomat built by Metior and a month ahead of the British Chubb MD2 from Smith Industries Chubb. It was on that Chubb MD2 that engineers at Smiths Group developed, in 1965, the idea of a PIN tied to the card, an invention credited to James Goodfellow. Both DACS and the Chubb MD2 accepted a single-use token or voucher, not a card with a magnetic stripe.

## Slide 13
ASK THE CLASS
Who invented the ATM?
Notes: No single person, and no single country. In 1960 Luther Simjian patented the Bankograph, a machine that accepted coins, cash and cheques but could not dispense money; an experimental unit was installed in New York by the City Bank of New York in 1961 and removed six months later for lack of customer interest. The machine generally credited as the first true ATM is the one installed by John Shepherd-Barron's team in Enfield in 1967. The idea of the PIN is credited to James Goodfellow, who filed the British patent in May 1966 together with Anthony Davies. In the United States, Donald Wetzel and Docutel were recognized by the Smithsonian in 1995 as the inventors of the networked ATM, one linked to a central system rather than tied to a single, isolated branch.

## Slide 14
04
CHAPTER
The chip and the frauds
What it really protects, and what it does not

## Slide 15
MAGNETIC STRIPE AGAINST CHIP
Magnetic stripe
THE CODE
Always the same
IF IT IS COPIED
Reusable forever
EMV chip
THE CODE
New every transaction
IF IT IS COPIED
It cannot be reused
The EMV cryptogram makes cloning a card far harder.
Notes: The EMV standard is named after its original backers, Europay, Mastercard and Visa, and it governs how chip cards work. Chip technology validates the card's authenticity and generates, for every single transaction, a one-time security code known as a cryptogram, which cannot be reused afterward. The number stored on a magnetic stripe never changes, so copying it with a skimmer is enough, on its own, to reuse it indefinitely.

## Slide 16
THREE NUMBERS WORTH KEEPING
15.6
billion EMV cards: in circulation, September 2026
96%
of in-store transactions: in more than 80 countries
50
euros, the liability cap: on unauthorized transactions
Notes: According to figures published by EMVCo, the organization owned by the major international payment networks that manages the EMV specifications, more than 15.6 billion EMV cards were in circulation worldwide as of September 2026, powering 96% of in-store transactions in more than 80 countries. Keep in mind that this figure is self-reported by the organization that manages the standard, and not an independent third-party estimate. The third number is about losing a card, regulations cap the cardholder's liability at 50 euros for unauthorized transactions, as long as they are reported to the bank promptly.

## Slide 17
THE THREE MOST COMMON FRAUDS
Skimming
Copies the card data
Hidden reader and tiny camera
Card trapping
Copies nothing at all
Jams the card in the reader
Jackpotting
A physical attack on the ATM
Cash dispensed with no transaction
Notes: Skimming means a hidden device placed over the card slot, often paired with a tiny hidden camera aimed at the keypad to capture the PIN. Card trapping, sometimes called a Lebanese loop, jams the card inside the reader; the customer assumes it is lost and walks away, and the criminal retrieves it afterward. It has seen a resurgence in regions like Europe, where chip-and-PIN cards have become more common, because it copies no data at all, and that is exactly why EMV alone cannot stop it. Jackpotting is a physical attack on the machine, forcing it to dispense cash without any authorized transaction. The U.S. Secret Service recommends preferring ATMs inside bank branches or near drive-up windows, checking for signs of tampering such as broken lights or a keypad that looks raised or loosely attached, and always covering the keypad with your hand while entering a PIN. If a card is stolen, Banca d'Italia advises calling the bank's hotline right away to block it and only then filing a police report.

## Slide 18
TEST YOURSELF · FOR THE CLASS
How does an ATM ask the bank for permission?
A Through the international ISO 8583 standard
B Through a phone call handled by a human operator
C It does not ask: it decides on its own
Notes: Answer: A. The authorization request travels from the ATM, through a chain of networks, to the issuing bank's system, formatted according to ISO 8583, the same standard behind Mastercard and Visa authorization messaging and the one point-of-sale terminals use in stores. If there is time, a second question from the Recap quiz: true or false, now that chip-and-PIN cards are widespread, card trapping has essentially disappeared? (False: it has seen a resurgence in exactly those regions where chip-and-PIN cards have become more common.)

## Slide 19
AND NOW, THE REVIEW
Clear in 30 seconds.
Yours in 10 minutes.
A 5-question quiz and 8 flashcards: recaplica.com/en/technology/how-atms-work/
Sources: Wikipedia · EMVCo · U.S. Secret Service · Banca d'Italia
Notes: To review, the online Recap has a 5-question quiz and 8 flashcards, with the full list of sources at the bottom of the page.