## Slide 1
TECHNOLOGY · RECAP
The microwave oven
Radio waves, water molecules and heat from friction
Notes: A microwave oven doesn't heat with a flame or a glowing heating coil. The heart of the appliance is a component called a magnetron, which turns electricity into high-power radio waves about 12 centimeters long. We will look at how the wave heats water, why metal behaves in two opposite ways, what the safety science says, and how all of it was discovered by accident.

## Slide 2
WHERE WE START
Where is the flame inside a
microwave oven?
Notes: There isn't one. Open the door and a microwave oven doesn't hide a flame or a glowing heating coil. The heart of the appliance is a component called a magnetron, which draws electricity from the wall outlet and turns it into high-power radio waves, about 12 centimeters long. The heat doesn't come from an already-hot source the way a conventional oven or a stovetop burner works, it starts inside the food.

## Slide 3
WHAT WE WILL COVER
01
The wave that heats water
02
Metal, mirror and spark
03
Non-ionizing radiation
04
A discovery by accident

## Slide 4
FROM THE WALL OUTLET TO THE HEAT
Magnetron
radio waves about 12 cm long
Vibration
faster vibration, more heat
Electricity
from the outlet
Water molecules
absorb the waves
Heat
through friction
Notes: The magnetron draws electricity from the wall outlet and turns it into high-power radio waves, about 12 centimeters long. As these microwaves pass through food, the water molecules inside absorb them and start vibrating faster, and the faster they vibrate the more heat is generated, through friction, not through contact with an already-hot source. The interior walls of the cooking chamber, flat and continuous, bounce the waves from one side to the other like a row of small mirrors, directing them toward the food instead of letting them scatter.

## Slide 5
TWO WAYS OF HEATING
Conventional oven
THE PRINCIPLE
Hot air, by convection
WHAT HEATS FIRST
The air, then the surface
Microwave oven
THE PRINCIPLE
Waves absorbed by water
WHAT HEATS FIRST
The water in the food
A conventional oven heats the air, a microwave heats the water in the food directly.
Notes: A conventional oven heats food with hot air, by convection and radiation, so the air in the cooking chamber warms up first and then the food's surface, and it needs preheating. In a microwave the waves are absorbed directly by the water and the other polar molecules in the food, with no preheating and shorter cooking times. Surface browning, typical of prolonged high heat, is generally absent, except with combined grill functions.

## Slide 6
ONE METAL, THREE BEHAVIORS
The walls
Flat, continuous metal
Bounce the waves onto the food, like mirrors
The fork
Isolated metal, sharp edges
Concentrates the field and strikes an arc
The flat sheet
Foil laid flat, or a pan
Reflects the waves away from the food
Notes: The oven's walls are broad, edge-free surfaces, they reflect an electric field that stays fairly evenly distributed and direct the microwaves toward the food. An isolated metal object, like a fork or a crumpled piece of aluminum foil, has sharp edges and tight folds, and that's where the electric field concentrates until it becomes strong enough to produce a visible arc, the spark. A flat pan or a flat sheet of aluminum foil simply reflects the microwaves away from the food, resulting in uneven cooking on top of the risk of damaging the appliance. Glass, ceramic without metallic trim, or plastic labeled microwave-safe work better.

## Slide 7
FALSE MYTH
Food does not come out radioactive.
Microwaves are non-ionizing radiation, with enough energy to make molecules vibrate but not enough to alter them chemically, unlike X-rays.
Notes: According to the FDA and the EPA, microwaves belong to the category of non-ionizing radiation, they have enough energy to move atoms and molecules, making them vibrate, but not enough to alter them chemically or strip away electrons, the way X-rays or gamma rays do. The absorbed energy turns into heat, and microwaves only exist while the oven is running, they don't stay trapped in the food or the appliance after it's switched off.

## Slide 8
THE REAL RISK ISN'T THE RADIATION
5
mW/cm²: the U.S. legal cap on leakage, at about 5 cm from the oven's surface
Heat
the most common risk: burns from food or liquids hotter than expected
Cold
the spots left behind: where uneven cooking lets bacteria survive
Notes: By law, in the United States a microwave oven can't leak more than 5 milliwatts of microwave radiation per square centimeter, measured at about 2 inches, or 5 centimeters, from the appliance's surface, for its entire working life, and that is the federal rule 21 CFR 1030.10. The oven is also built with safety interlocks that shut it off as soon as the door opens. The most common practical risk isn't the radiation but the heat, with burns from food or liquids that come out hotter than expected, and uneven cooking can leave cold spots where bacteria survive. Stirring the food, rotating the plate and letting it stand for a few minutes helps the heat spread.

## Slide 9
WHO FOUND IT
Percy Spencer
Raytheon, 1945
1940s
Magnetrons for military radar
1945
A candy bar melts in his pocket
1965
Raytheon acquires Amana Refrigeration
Notes: In the 1940s Percy Spencer was an engineer and vice president at Raytheon, an American company that built magnetrons for World War II military radar. In 1945, working near a running magnetron, he noticed a candy bar in his pocket had melted. He tried popcorn kernels, which popped, and then an egg, which exploded. Those tests led to the first commercial microwave oven, called the Radarange. Widespread home use came after Raytheon acquired Amana Refrigeration in 1965.

## Slide 10
AND NOW, THE REVIEW
Clear in 30 seconds.
Yours in 10 minutes.
A 5-question quiz and 8 flashcards: recaplica.com/en/technology/how-microwave-ovens-work/
Sources: FDA · EPA · National Inventors Hall of Fame · Clemson University · Harvard Health Publishing
Notes: To review, the online Recap has a 5-question quiz and 8 flashcards, with the full list of sources at the bottom of the page.