## Slide 1
TECHNOLOGY · RECAP
Isometric drawing
120° angles, one scale on every axis
Notes: Isometric drawing is the most regular of the axonometric projections, with equal angles and equal scale. Today: what it is, how to build it starting from a cube, how it compares with dimetric and oblique projection, and where it's actually used.

## Slide 2
120° ANGLES ON EVERY AXIS
A cube drawn this way
never looks distorted. Why
not?
Notes: Because the scale factor is identical on all three axes: no direction shrinks more than the others, so the cube keeps the same proportions on every face.

## Slide 3
FROM THE ANGLE TO THE FINISHED DRAWING
01
What it is
02
How to construct it
03
Comparing the three
04
Where it's actually used

## Slide 4
THE SAME MEASURE IN THREE DIRECTIONS
120°
between every pair of axes: the same tilt on every side
1
single scale for all three axes: no direction shrinks more than the others
Greek
where the name comes from: the word means equal measure
Notes: The three coordinate axes are projected shortened by the same amount, and the angle between any pair of them is always 120°. The word isometric comes from Greek and means equal measure: the scale along each axis of the projection matches the other two.

## Slide 5
NO VANISHING POINT
Do isometric objects shrink
as they move further away?
Notes: No: in parallel projections like isometric drawing, dimensions don't change with distance from the viewer, unlike in perspective drawing with its vanishing points.

## Slide 6
FROM THE AXES TO A ROTATED CUBE
Axis z
vertical, the starting point
Axes x and y at 120°
one right, one left of z
Rotated cube
about 45°, then about 35°
Notes: The construction starts from the vertical axis z; the other two axes are drawn tilted 120° from z, one to the right and one to the left. The same drawing can also be reached by rotating a cube about 45° around the vertical axis and then about 35.264° around a horizontal one.

## Slide 7
EQUAL ANGLES
Isometric
120° everywhere
Same scale on all three axes
UNEQUAL ANGLES
Dimetric
90° X and Y
120° and 150° with axis Z
ONE DIFFERENT AXIS
Oblique
45° axis Y
Measurements on Y are halved
Notes: In dimetric projection the angle between X and Y stays at 90°, while the other two open to 120° and 150° with axis Z. In oblique projection axis X stays at 90° with Z, but measurements along axis Y, tilted at 45°, are halved by convention. In isometric drawing the plane of projection is tilted equally relative to all three principal planes of the object, while in oblique projection the plane stays parallel to one face.

## Slide 8
SAME PROJECTION, TWO USES
Technical drawing
MANUALS
Assembly diagrams
ADVANTAGE
Whole part, real measurements
Video games
PIXEL ART
Block-built environments
ADVANTAGE
No true perspective needed
The same 120° projection builds technical manuals and game environments alike.
Notes: In technical manuals isometric projection shows a whole part with correct proportions between its pieces; the same 120° projection also turns up in video games and pixel art, standing in for a calculated true perspective.

## Slide 9
0.816 TIMES THE REAL MEASUREMENT
Isometric doesn't mean full scale.
A true isometric projection shrinks every measurement to 0.816 times the real one, a 2:3 ratio; in practice, drafters often work at real scale instead, producing an isometric drawing.
Notes: The isometric-looking drawing seen in technical manuals often carries real measurements rather than shrunk ones: the result is slightly larger than a true isometric projection, but with correct proportions between the axes.

## Slide 10
NOW FOR THE REVIEW
Clear in 30 seconds.
Yours in 10 minutes.
A 5-question quiz and 8 flashcards: recaplica.com/en/technology/isometric-drawing/
Sources: Wikipedia · Wikipedia IT · Educazione Tecnica Online · The Engineer's Post
Notes: To review, the online Recap has a 5-question quiz and 8 flashcards, with the full sources listed at the bottom of the page.