## Slide 1
TECHNOLOGY · RECAP
Manual and automatic transmissions
What really happens between engine and wheels
Notes: A manual transmission uses a disc clutch and gears that the driver engages by hand, while a traditional automatic shifts on its own using a hydraulic torque converter and planetary gear sets controlled by a computer. Newer designs have joined those two classic layouts, the dual-clutch transmission and the belt-driven CVT. We will look at how each one works, and at why the choice differs from market to market.

## Slide 2
FIRST QUESTION
Who picks the gear, the
driver or the computer?
Notes: In a manual gearbox the driver decides when to shift and operates the clutch with a dedicated pedal. In a traditional automatic the driver does not have to do anything, because a hydraulic valve body decides when to shift, guided by sensors that read engine load, road speed and throttle position.

## Slide 3
FOUR STOPS
01
The manual gearbox
02
The traditional automatic
03
The modern variants
04
Fuel, cost, geography

## Slide 4
01
CHAPTER
The manual gearbox
Clutch, gears, synchronizers

## Slide 5
WHAT HAPPENS ON EVERY SHIFT
Clutch
between flywheel and plate
Gears
always in constant mesh
Pedal down
the disc leaves the flywheel
Synchronizers
they match the speeds
Gear engaged
the dog clutch locks it
Notes: The clutch is a disc sitting between the engine's flywheel and the transmission's pressure plate, and when the pedal is pressed the disc separates from the flywheel and cuts off torque flow to the gears. Inside the gearbox housing, a modern car typically has three shafts, an input shaft connected to the clutch, a countershaft, and an output shaft that sends torque to the wheels. The gears stay in constant mesh and spin freely on the output shaft until a sliding dog clutch locks one of them in place; before that lock-up happens, conical synchronizer rings match the rotational speed of the gear to that of the shaft, and this mechanism is what prevents the grinding noise typical of older gearboxes.

## Slide 6
MILESTONES
The manual gearbox
1891-2012
1891
First three-speed, Panhard et Levassor
1919
Thompson patents the synchronizer
1928
First production synchronizer, a Cadillac
2012
First seven-speed, Porsche 911
Notes: The earliest car gearboxes, from the late 1800s through the early 1900s, had no synchronizers at all, they were sliding-mesh designs informally known as crash boxes for the racket the gears made as they slammed together during a shift. The synchronizer was patented in 1919 by Earl Avery Thompson and first appeared on a production car in 1928, on a Cadillac; it was not until 1952, with the Porsche 356, that a car had synchronizers on every forward gear rather than just the higher ones. Five-speed gearboxes spread widely in the 1980s, six-speeds appeared on sports cars in the early 1990s, and the first seven-speed manual debuted on the 2012 Porsche 911.

## Slide 7
02
CHAPTER
The traditional automatic
Torque converter and planetary gears

## Slide 8
INSIDE THE TORQUE CONVERTER
Impeller
Bolted to the engine flywheel
As it spins, it drives the fluid
Turbine
On the transmission input shaft
The fluid sets it in motion
Stator
Multiplies engine torque
At low speed it sends fluid back to the impeller
Notes: A traditional automatic has no driver-operated disc clutch, and in its place sits a torque converter, a hydraulic component built from three parts. The impeller is bolted to the engine's flywheel and, as it spins, drives the transmission fluid; the turbine, connected to the transmission's input shaft, is set in motion by that fluid; the stator, positioned between the two, redirects the flow. At low speed the stator stays still and sends the fluid back toward the impeller, multiplying engine torque; as engine speed rises, the stator starts spinning freely and the converter behaves like a simple fluid coupling, with no more torque multiplication.

## Slide 9
THE FIRST MASS-PRODUCED AUTOMATIC
1939
the year it launched: GM's Hydra-Matic Drive, for the 1940 model year
57
dollars on the Oldsmobile: about 1,310 dollars in 2025 money
1
million units: sold by 1949, after nearly 200,000 by 1942
Notes: The first mass-produced automatic transmission for passenger cars was General Motors' Hydra-Matic Drive, developed by a team led by the same Earl Thompson who had invented the manual gearbox's synchronizer. The project started as a Cadillac program in 1932, moved to GM's research division in 1936, and entered production in May 1939 for the 1940 model year; the first equipped cars, the Oldsmobile Series 60 and 70, shipped in October 1939. It became available on Cadillac in 1941, nearly 200,000 units had been sold by the time civilian car production stopped for the war in February 1942, and a million had been sold by 1949. Versions of the same transmission were also fitted to US military vehicles in World War II, including the M5 Stuart and M24 Chaffee light tanks.

## Slide 10
03
CHAPTER
The modern variants
Dual-clutch, CVT, automated manuals

## Slide 11
CONTINUOUS RATIO
CVT
1958 DAF 600
A belt between two variable pulleys
AUTOMATED MANUAL
Selespeed
1999 Alfa 156
Manual gearbox, automated clutch
DUAL-CLUTCH
DSG
2003 Golf R32
Even and odd gears, two clutches
Notes: Between the pure manual and the torque-converter automatic sits a third family, automated manuals, mechanically manual gearboxes with a conventional clutch in which an electro-hydraulic actuator handles both the shifting and the clutch instead of the driver; the Selespeed, introduced in 1999 on the Alfa Romeo 156 and developed by the Italian supplier Magneti Marelli, could run in a sequential mode or in a city mode that made it behave like a full automatic. The dual-clutch transmission uses two separate clutches for the even and odd gears, so while one is engaged the other has already lined up the next ratio; the concept was first sketched out in 1939 by French engineer Adolphe Kégresse, Porsche developed it for racing from the late 1970s and tested its PDK on a 956 in 1983, and it reached the general public in 2003 with the European Volkswagen Golf R32 and its DSG gearbox. The CVT has no fixed gears at all, and the first mass-production car to use one was the Dutch DAF 600 in 1958; in 1987 Subaru fitted the Justy with the first electronically controlled steel-belt CVT, and in 1997 the Toyota Prius introduced the Toyota Hybrid System.

## Slide 12
FIXED RATIOS, OR CONTINUOUS
Traditional automatic
HOW RATIOS ARE MADE
Planetary gear sets
HOW MANY GEARS
A fixed number
Belt-driven CVT
HOW RATIOS ARE MADE
A belt between pulleys
HOW MANY GEARS
No fixed gears at all
One works in steps, the other changes ratio continuously.
Notes: A traditional automatic produces its fixed ratios with planetary gear sets, a sun gear at the center, an outer ring gear and a set of planet gears rotating between the two; locking one element of the gear set while driving another produces a different ratio, and a three-speed automatic typically combines two planetary gear sets. A CVT instead uses a V-belt running between two variable-diameter pulleys, and moving the pulley halves closer together or farther apart changes the ratio continuously, with no perceptible shift steps. A belt-driven CVT reaches a mechanical efficiency of around 88%, often offset by the fact that the engine can keep running at its most efficient speed; the downside drivers complain about most is the rubber-band feel under acceleration.

## Slide 13
04
CHAPTER
Fuel, cost, geography
The numbers, market by market

## Slide 14
FALSE MYTH
Automatics no longer use more fuel.
In 1990 automatics used 5% more fuel on average than equivalent manuals. By 2022, according to EPA data, they were using 5% less.
Notes: The efficiency crossover, according to data from the US Environmental Protection Agency, happened around 2010-2012. The deciding factor is the number of available ratios, because in 1980 the market was dominated by three-speed automatics, by 1999 four-speed automatics were standard on more than 80% of vehicles, and modern automatics commonly offer 8, 9 or even 10 gears against a typical maximum of 6 for a manual. More gears mean more chances to keep the engine close to its ideal operating speed. These are market averages recorded by the EPA, not a verdict on any single car.

## Slide 15
WHERE EACH ONE IS DRIVEN
<1%
of new US cars: in model year 2023, down from nearly 35% in 1980
29%
of new registrations: across Europe's five largest markets, in 2024
7.45
dollars a gallon, roughly: gasoline in Germany, against about 3 in the US
Notes: In the United States the share of new cars with a manual transmission fell below 1% starting with model year 2021, down from nearly 35% in 1980; in Europe, by contrast, manuals still accounted for close to 29% of new registrations across the continent's five largest markets in 2024. Fuel economy is not the only factor at play, because gasoline in Germany costs around 7.45 dollars a gallon against a US average of roughly 3 dollars, and in some European countries, such as the United Kingdom, manual and automatic licenses are issued separately, so drivers who learn on a manual can also drive an automatic but not the other way around. The result is that manufacturers have to keep building different transmissions for markets with very different driving habits.

## Slide 16
WHAT UPKEEP COSTS
Manual
OIL CHANGE
About half the other
FULL REPLACEMENT
1,500-3,000 dollars
Automatic
FLUID CHANGE
100 to 200 dollars
FULL REPLACEMENT
2,000-4,000, remanufactured
A CVT replacement can flip that comparison on its head.
Notes: An oil change on a manual typically costs about half of what a fluid change costs on an automatic, which runs from 100 to 200 dollars; a full transmission replacement on a non-luxury vehicle costs 1,500 to 3,000 dollars for a manual, against 2,000-4,000 dollars for a remanufactured automatic. CVTs, though, can flip that comparison on its head, because replacing one on a Nissan Sentra has been estimated at around 4,000 dollars, versus roughly 2,500 dollars for the six-speed automatic in a Chevrolet Cruze. Driving style also weighs on a manual's costs, because aggressive clutch use wears it out far faster than individual driving habits affect an automatic.

## Slide 17
TEST YOURSELF · FOR THE CLASS
In what year did dual-clutch reach the general public?
A 1981
B 1999
C 2003
Notes: Answer C, 2003. The dual-clutch concept dates back to 1939, and Porsche developed it for racing starting in the late 1970s, but it was the 2003 Volkswagen Golf R32, with its DSG gearbox, that first brought it to a mass-production car for everyday drivers. If there is time, a second question from the Recap quiz, what does the stator do inside a torque converter at low speed? (It redirects the transmission fluid back toward the impeller, multiplying engine torque.)

## Slide 18
NOW, THE REVIEW
Clear in 30 seconds.
Yours in 10 minutes.
A 5-question quiz and 8 flashcards: recaplica.com/en/technology/manual-vs-automatic-transmission/
Sources: EPA · The Autopian · SlashGear · Cars.com · How A Car Works
Notes: To review, the Recap online has a 5-question quiz and 8 flashcards, with all the full sources at the bottom of the page.