## Slide 1
TECHNOLOGY · RECAP
Monometric Axonometric Projection
Drawing an object in three dimensions, with no reduction on any axis
Notes: Welcome. Today we look at how one of the most widely used axonometric projections in Italian school technical drawing gets built.

## Slide 2
IN ITALIAN SCHOOL CURRICULA
Monometric and isometric:
same drawing, two different
names?
Notes: The answer isn't as clean as it sounds: some sources say they're synonyms, other school textbooks treat them as two different things. We'll get to that further on.

## Slide 3
ANGLES, MEASUREMENTS, CONSTRUCTION, NAME
01
What it is and how it's classified
02
The axes and their angles
03
How it's built, step by step
04
One name, two uses: monometric or isometric?
Notes: We start from the classification, then the axis angles, then the construction, and we close with the question of the name.

## Slide 4
SAME PRINCIPLE, DIFFERENT PICTURE PLANE
Monometric
PICTURE PLANE
Horizontal
MEASUREMENTS
True scale, no reduction
Cavalier
PICTURE PLANE
Vertical
MEASUREMENTS
Reduced on depth
The picture plane's orientation changes, and so does how measurements are treated
Notes: Monometric projection uses a horizontal picture plane and transfers measurements without reduction on any axis. Cavalier projection uses a vertical picture plane and reduces measurements on the depth axis.

## Slide 5
THIRTY, SIXTY, ONE HUNDRED TWENTY DEGREES
30°
angle of the x-axis from the horizontal: undefined
60°
angle of the y-axis from the horizontal: undefined
120°
angle between the x-axis and the vertical z-axis: undefined
Notes: The z-axis stays vertical. The x-axis tilts 30°, the y-axis 60° from the horizontal: the two end up perpendicular to each other, and between x and z the angle is 120°.

## Slide 6
IN THE CONVENTIONAL VARIANT
The floor plan
Drawn in the horizontal plane, at true proportions
The heights
Raised from the base points, along the vertical axis
The hidden lines
Drawn as dashes
Notes: This procedure is described for the variant called 'conventional monometric,' which uses a different picture plane from the 30°/60° one. The principle still helps as a guide: base first, then heights, then the lines the solid hides.

## Slide 7
ACCORDING TO ONE ACADEMIC SOURCE
One drawing, two names not every textbook uses the same way
When the axes form equal angles with the picture plane, one academic source calls that by the same name as the oblique construction at 30°/60°/120°, but that one is an orthogonal projection with reduced measurements; other Italian school textbooks instead treat 'monometric' and 'isometric' as distinct constructions
Notes: It's not a settled point: a student in Italy can run into either version, depending on the textbook or the program.

## Slide 8
WHAT IT'S USED FOR
Mechanical parts
Industrial technical drawing
Components to represent in three dimensions
Machines
Industrial technical drawing
Assemblies and functional units
Architecture
Project views
Buildings and spaces shown in volume
Notes: The same type of axonometric projection serves both industrial technical drawing, for mechanical parts and machines, and architectural project views.

## Slide 9
TRY ANSWERING
What is the angle between the x-axis and the vertical z-axis, in the most common scheme?
A 90°
B 120°
C 60°
Notes: The answer is 120°, because the x-axis is drawn at 30° from the horizontal and the z-axis stays vertical. Second question for the class: at how many degrees from the horizontal is the y-axis drawn? Answer: 60°.

## Slide 10
NOW, FOR REVIEW
Clear in 30 seconds.
Yours in 10 minutes.
Review with the Recap's quiz and flashcards recaplica.com/en/technology/monometric-axonometric-projection/
Sources: AliceAppunti · unmondoacolori · Treccani · UNI · larapedia
Notes: The full Recap also has the concept map and the most common misconceptions about this topic.