## Slide 1
TECHNOLOGY · RECAP
Orthographic Projection
One object, three views
Notes: Orthographic projection is how technical drawing shows a three-dimensional object using several flat views: top, front, and side. Today we cover what the planes are, how the views get arranged, and how to draw a solid.

## Slide 2
TAKE A GUESS
How do you draw a cube
without using perspective?
Notes: You break the solid into separate flat views, each projected onto a plane at a right angle to the direction you're looking from. That's the core idea behind orthographic projection, as opposed to perspective drawing with vanishing points.

## Slide 3
WHAT'S AHEAD
01
The three projection planes
02
The three views
03
First-angle and third-angle projection
04
How to draw a solid

## Slide 4
01
CHAPTER
The three projection planes
Horizontal, vertical, profile

## Slide 5
THE PLANES AND THEIR ROLES
H
horizontal plane: receives the top view
V
vertical plane: receives the front view
P
profile plane: receives the side view
Notes: The three standard projection planes are horizontal, vertical, and profile. Set at right angles to each other, they form what's known as Monge's trihedron.

## Slide 6
02
CHAPTER
The three views
Top, front, side

## Slide 7
FROM ABOVE
Top view
H plane
View projected onto the horizontal plane
HEAD ON
Front view
V plane
View projected onto the vertical plane
FROM THE SIDE
Side view
P plane
View projected onto the profile plane
Notes: The top view looks straight down onto the horizontal plane, the front view looks straight ahead onto the vertical plane, and the side view looks from left or right onto the profile plane.

## Slide 8
03
CHAPTER
First angle or third angle
Same view, opposite placement

## Slide 9
SAME OBJECT, SWAPPED VIEWS
First-angle projection
ANGLE
First angle
RIGHT-SIDE VIEW
Goes left
Third-angle projection
ANGLE
Third angle
RIGHT-SIDE VIEW
Goes right
Europe uses first-angle projection
Notes: In first-angle projection, the standard across Europe, each view sits on the opposite side from the face it shows: the view from the right goes to the left of the front view. In third-angle projection, standard in the US, the projection plane is pictured as glass between the viewer and the object, and the same view sits on the matching side: the view from the right goes to the right.

## Slide 10
THE FOLDING TRICK
Fold one plane onto another and the shape in space comes back.
Top, front, and side views stay separate flat drawings on the page; folding one onto another recovers the solid's shape and measurements, and the process works in reverse too.
Notes: Folding one of the two original planes onto the other lets you reconstruct the shape and dimensions of a figure in space, and the reverse works too — that's the principle behind Monge's two-plane projection.

## Slide 11
04
CHAPTER
How to draw a solid
Visible edges and hidden edges

## Slide 12
FROM THE SOLID TO THREE VIEWS
Pick the faces
which one faces front, up, and sideways
Project the edges
onto the horizontal, vertical, and profile planes
Tell lines apart
solid or dashed
Notes: For a rectangular box, you project the edges onto the three planes: the front face onto the vertical plane gives the front view, the top face onto the horizontal plane gives the top view, and the side face onto the profile plane gives the side view. Edges covered by another face are drawn dashed.

## Slide 13
FOR THE CLASS
Looking at a rectangular box from the front, how do you draw the vertical edge at the back, hidden by the body of the solid?
A With a solid line
B With a dashed line
C It isn't drawn
Notes: The answer is the dashed line: edges hidden behind the solid are drawn that way, visible edges with a solid line. A follow-up for the class: in the front view of a cylinder, what gets projected instead of edges, since a curved solid doesn't have any?

## Slide 14
QUICK RECAP
Clear in 30 seconds.
Yours in 10 minutes.
Read the full Recap recaplica.com/en/technology/orthographic-projection/
Sources: Treccani · Wikipedia · tecnologiaduepuntozero.it · Studenti.it
Notes: Orthographic projection remains, in 2026, the basic method taught in technical drawing classes: three planes, three views, two different conventions for laying them out on the page.