## Slide 1
TECHNOLOGY · RECAP
The OSI Model
Seven layers so two computers can understand each other
Notes: The OSI model breaks network communication into seven abstract layers, according to IBM. This deck sets it side by side with TCP/IP, the four-layer model networks actually run on.

## Slide 2
TAKE A GUESS
How does a browser load a
page through cables,
routers, and computers it
has never met?
Notes: The answer is protocols. Each layer of a network model has one job, from the physical cable to the program the user sees, and the protocols at each layer speak the same language on both ends of the connection.

## Slide 3
IN THIS RECAP
01
The OSI model
02
The TCP/IP model
03
Where they meet
04
Protocols at work

## Slide 4
THE THREE LAYERS CLOSEST TO THE USER
7
Application: Starts the exchange with protocols like HTTP and DNS
6
Presentation: Translates, compresses, and encrypts data
5
Session: Opens and closes connections between devices
Notes: According to IBM, the Application layer (7) starts the conversation with the network and includes the protocols that turn data into responses the user can read. The Presentation layer (6) prepares that data through translation, compression, and encryption. The Session layer (5) opens and closes the connections between two devices talking to each other.

## Slide 5
A MODEL THAT NEVER RUNS ON A WIRE
OSI describes an idea, not software running in routers
Real networks run on TCP/IP, four layers of standardized protocols, according to IBM
Notes: OSI stays a conceptual model, useful for reasoning and teaching. The networks that actually carry data across the planet follow the TCP/IP architecture described in RFC 1122.

## Slide 6
A PACKET CROSSES FOUR LAYERS
Transport
End-to-end communication between applications
Application
Protocols like HTTP
Internet
Routes across different networks
Link
Delivers on the local network
Notes: RFC 1122 lists Application, Transport, Internet, and Link as the four layers of the Internet protocol suite. The Transport layer handles delivery between the two communicating applications, while the Internet layer uses IP to move data from the source host to the destination host.

## Slide 7
OSI AND TCP/IP SIDE BY SIDE
OSI
SEVEN LAYERS
A conceptual model (IBM)
5, 6, AND 7
Three separate layers
TCP/IP
FOUR LAYERS
Running in real networks (RFC 1122)
APPLICATION
Groups 3 OSI layers into one
The lower layers line up one to one, the upper ones merge into one
Notes: Cisco Networking Academy states that OSI's Network layer maps to TCP/IP's Internet layer, and OSI's Transport layer maps to TCP/IP's Transport layer. At the bottom of the stack, OSI keeps Data Link and Physical separate, which is why it's still the usual reference when talking about the lowest layers of a network.

## Slide 8
TYPICAL PROTOCOLS BY LAYER
HTTP
Application: A browser uses it to request a web page
TCP
Transport: Makes sure data arrives without loss
IPv4
Network: Routes packets between different networks
Notes: According to IBM, the Application layer runs HTTP, FTP, DNS, and SMTP; the Transport layer runs TCP and UDP; the Network layer runs IPv4 and IPv6; the Data Link layer runs Ethernet and ARP.

## Slide 9
FOR THE CLASS
How many layers does the TCP/IP model have, according to RFC 1122?
A Seven
B Four
C Five
Notes: The answer is four, Application, Transport, Internet, and Link. Second question for the class: which TCP/IP layer does OSI's Network layer correspond to? Answer, the Internet layer.

## Slide 10
NOW, THE RECAP
Clear in 30 seconds.
Yours in 10 minutes.
Read the Recap again and try the quiz recaplica.com/en/technology/osi-model/
Sources: IBM · RFC 1122 · Cisco Networking Academy
Notes: The seven-layer OSI model and the four-layer TCP/IP model describe the same network communication, at different scales.