## Slide 1
TECHNOLOGY · RECAP
The photovoltaic system
From sunlight to the current in the wall socket
Notes: A photovoltaic system turns sunlight into electricity through the photovoltaic effect, a physical process that happens inside cells made of semiconductor material, usually silicon. Today we will look at how the current is born, which families of cells exist, where a system can be installed and what its output depends on.

## Slide 2
WHERE WE START
How does sunlight turn into
electric current?
Notes: When sunlight strikes a semiconductor material, typically chemically treated silicon, it frees up electrons and generates a direct current, and that is the photovoltaic effect. Individual cells are assembled into a panel, the module; several panels are wired together in series to form a string; an inverter turns the direct current into the alternating current used by household appliances and fed into the grid.

## Slide 3
WHAT WE WILL COVER
01
From sunlight to current
02
The families of cells
03
Where a system goes
04
Output, lifespan, end of life

## Slide 4
01
CHAPTER
From sunlight to current
Photovoltaic effect, cell, module, inverter

## Slide 5
FROM THE CELL TO THE GRID
Direct current
born inside the cells
Inverter
turns it into alternating
Cell
silicon frees up electrons
Panel and string
panels wired in series
The grid
alternating current
Notes: Individual cells are assembled into a panel, the module; several panels are wired together in series to form a string; an inverter finally turns the direct current produced into the alternating current used by household appliances and fed into the grid. In a grid-connected system, electricity produced and not consumed right away is fed into the grid.

## Slide 6
TWO WAYS OF USING LIGHT
Photosynthesis
WHAT LIGHT BECOMES
Chemical energy
STEPS IN BETWEEN
The plant's chemistry
Photovoltaic effect
WHAT LIGHT BECOMES
Electric current
STEPS IN BETWEEN
None
Same sunlight going in, two completely different processes.
Notes: In photosynthesis, light becomes chemical energy stored in a sugar molecule. In the photovoltaic effect it becomes a flow of electrons that registers immediately as electric current, with no chemical steps in between.

## Slide 7
02
CHAPTER
The families of cells
Three generations, and a market that shifted

## Slide 8
FIRST GENERATION
Crystalline
98% of modules
Wafer-based silicon, in 2025
SECOND GENERATION
Thin film
2-3% of modules
CdTe, CIGS, amorphous silicon
THIRD GENERATION
Emerging
35.2% in tandem
A 2026 record, not yet mass market
Notes: In 2025, wafer-based silicon covered about 98% of world module production, while thin film accounted for between 2 and 3% of the market. Third-generation technologies are not yet significant in the mass market, but the laboratory record for a silicon tandem, as of 2026, stands at 35.2%, against 28.1% for a single monocrystalline silicon cell. Laboratory records should not be confused with the efficiency of commercial panels, which is always lower.

## Slide 9
HOW THE MARKET SHIFTED
706
GWp made in 2025: of which 690 GWp monocrystalline silicon
0
GWp polycrystalline: back in 2017 it was still about 48% of the market
~25%
commercial efficiency: of monocrystalline modules in 2026, up from 17% in 2016
Notes: World module production in 2025 totaled around 706 GWp, of which 690 GWp was monocrystalline silicon and zero was polycrystalline silicon, which has practically disappeared from large-scale industrial production. Average commercial efficiency of monocrystalline modules has risen from about 17% to just under 25% between roughly 2016 and 2026. The n-type TOPCon and Heterojunction technologies are replacing the older p-type PERC technology as the market standard.

## Slide 10
03
CHAPTER
Where a system goes
Roofs, ground, water and farmland

## Slide 11
THREE WAYS TO INSTALL A SYSTEM
Integrated
Replaces an architectural element
Roof tiles, canopies, brise-soleil
Partly integrated
Rests on the roof slope
Replacing nothing
Non-integrated
Typically ground-mounted
The large installations
Notes: The terminology (integrated, partially integrated, non-integrated) comes from Italy's old Conto Energia, the incentive program closed for good in 2013, and that program's tariffs no longer mean anything; the three categories are still useful for describing how a system is physically installed. A system can sit on a roof, a facade or the ground. More recent setups add to the picture, with agrivoltaic systems, which combine electricity generation with farming on the same land, and floating systems on bodies of water.

## Slide 12
ON THE GRID, OR OFF IT
Grid-connected
HOW COMMON
98% at low voltage
THE ELECTRICITY
Fed into the grid, and sold
Stand-alone
WHAT THEY ARE
Off-grid, for specific needs
THE ELECTRICITY
Used on the spot
Where the grid does not reach, the current is used on site.
Notes: The large majority of systems in Italy are grid-connected, and 98% of Italian systems are connected at low voltage according to the 2024 IEA-PVPS report; electricity produced and not consumed right away is fed into the grid and can be sold. Stand-alone systems are not connected to the grid and generate direct current used directly for specific needs, such as water pumping, lighting or refrigeration, typically at sites without a grid connection.

## Slide 13
HOW MUCH SOLAR ITALY HAS INSTALLED
45 GW
cumulative capacity: nearly reached in March 2026, from 37 GW in 2024
1.88
million systems: across the country by the end of 2024, 55% in the north
11.5%
of electricity use: covered by solar in 2024, with 36 TWh generated
Notes: According to the IEA-PVPS report on Italy, cumulative national capacity stood at 37 GW at the end of 2024, with 6.7 GW added during the year and 278,423 new systems, for a total of 1.88 million installations across the country; 55% of them are located in northern Italy. In 2024, solar power generated 36 TWh of electricity, about 11.5% of national electricity consumption, and the national plan cited in the report targets 80 GW by 2030. By the end of March 2026, cumulative capacity had nearly reached 45 GW. Anyone installing a photovoltaic system or a storage battery must notify ENEA; for storage systems alone, this requirement has applied since January 1, 2019. On incentives, for spending in 2025 and 2026 the Irpef deduction is worth 50% on a main home and 36% in other cases, with a 96,000 euro spending cap; electricity fed into the grid is sold to the GSE under the Ritiro Dedicato scheme, since Scambio sul Posto closed to new entrants in 2025.

## Slide 14
04
CHAPTER
Output, lifespan, end of life
Orientation, tilt, 25 years of service

## Slide 15
WHAT THE OUTPUT DEPENDS ON
180°
the azimuth: south, the direction with the most direct sunlight
15-20%
the estimated loss: from facing panels east or west instead of south
PVGIS
the free tool: from the European Commission, it computes tilt and orientation
Notes: In Italy the optimal orientation is generally south, 180° azimuth, because at this latitude that is the direction from which the most direct sunlight arrives over the course of the day. The optimal tilt is not a single number that works everywhere, it varies with the latitude of the site and shifts slightly with trees, nearby buildings or mountains on the horizon. PVGIS, developed by the Joint Research Centre of the European Commission, is free and needs no registration, estimates expected output for any point on the globe from satellite irradiance data covering 2014-2024, and includes the Optimize slope and Optimize slope and azimuth functions.

## Slide 16
FALSE MYTH
Clouds do not switch the panels off.
Cells respond to diffuse sunlight too, not just direct light. Under an overcast sky output drops, but it does not disappear.
Notes: It is the same physical principle behind PVGIS calculations, which factor in both direct and diffuse irradiance. A second false myth is about geography, since solar power is not a southern Italian affair only, and in fact 55% of the country's photovoltaic systems are located in northern Italy, according to the IEA-PVPS report.

## Slide 17
WHAT A PANEL IS MADE OF, AND HOW LONG IT LASTS
25
years of service life: the Fraunhofer ISE assumption, with 0.70% degradation a year
65.8%
glass: plus 17.5% aluminum, recyclable at 100%
1 year
the energy payback time: for a system in Sicily with crystalline silicon modules
Notes: By weight, a crystalline silicon panel is made mostly of glass, 65.8% and recyclable at a 97% rate, and aluminum, 17.5% and recyclable at 100%, plus EVA, silicon and copper. According to a 2020 ENEA technical report, about 90% of a panel's weight is made of materials classified as non-hazardous, and modern technology can recover between 75 and 100% of the materials at end of life. The harmonized Fraunhofer ISE assumptions put service life at 25 years with an average degradation rate of 0.70% per year; a system in Sicily recovers the energy spent building it in about a year, and over the following 20 years it can produce up to 20 times the energy invested.

## Slide 18
TEST YOURSELF · FOR THE CLASS
Why do south-facing panels produce more in Italy?
A Because at that latitude they get the most direct sunlight
B Because a national regulation requires panels to face south
C Because the GSE pays more for electricity from those systems
Notes: Answer A. At Italy's latitude the sun tracks across the sky mostly to the south, so a panel facing that direction intercepts the most direct sunlight during the day; a purely east- or west-facing system loses an estimated 15-20% of production, based on simulations using PVGIS data. If there is time, a second question from the Recap quiz, what sets a stand-alone system apart from one connected to the grid? (It is not connected to the public grid and generates direct current used on the spot, for water pumping, lighting or refrigeration.)

## Slide 19
AND NOW, THE REVIEW
Clear in 30 seconds.
Yours in 10 minutes.
A 5-question quiz and 8 flashcards: recaplica.com/en/technology/photovoltaic-system/
Sources: Fraunhofer ISE · PVGIS (European Commission) · ENEA · IEA-PVPS · Italian Revenue Agency
Notes: To review, the online Recap has a 5-question quiz and 8 flashcards, with the full list of sources at the bottom of the page.