## Slide 1
TECHNOLOGY · RECAP
The robot vacuum
How it knows where it is, and where it has not been yet
Notes: A robot vacuum is a small autonomous appliance that cleans your floors without being pushed by hand, finding its way around with sensors and returning to its dock on its own to recharge. In this presentation we look at where the machine came from, how it manages to vacuum on very little power, which sensors tell it what is around it, and how it moved from random movement to real maps of the home.

## Slide 2
THE REAL QUESTION
How can a robot clean a
home it cannot see?
Notes: A robot vacuum does not have vision the way we think of it, but it adds up data from several sensors to figure out where it is and what is around it. The earliest models estimated their own position blindly, combining wheel rotation and inertial unit data, a technique known as dead reckoning. From 2010 onwards lasers, and from 2015 cameras, let the robot build a real map of the room instead.

## Slide 3
HOW WE PROCEED
01
Before the Roomba
02
Three watts of suction
03
Seeing without eyes
04
From random to a map

## Slide 4
01
CHAPTER
Before the Roomba
A 1956 novel, and an unlucky pioneer

## Slide 5
ORIGINS
The long wait
1956-2002
1956
Heinlein imagines it in a novel
1985
Tomy's Dustbot, with built-in suction
2001
The Trilobite, the first one ever
2002
The Roomba, the first to succeed
Notes: In 1956 science fiction writer Robert Heinlein described a device in The Door into Summer that roamed the house all day looking for dirt. A year later engineer Donald Moore patented several robotic home appliances, including an automatic sweeper, but Whirlpool decided against building it after a 1959 demonstration. In 1985 came Tomy's Dustbot, described as the first robot with built-in suction. Electrolux showed off a prototype of its Trilobite on TV as early as 1996, but the actual commercial launch came in 2001, making it the first true commercial robotic vacuum cleaner in history; serious navigation problems, though, got it pulled from the market. Meanwhile, at MIT, Joe Jones had been working on the idea since 1989, and only in 1999, inside the fledgling iRobot, was Scamp born, the oldest documented prototype, funded by S.C. Johnson before the company stepped away.

## Slide 6
TWO DIFFERENT FIRSTS
Trilobite, 2001
THE CLAIM
The first one ever
HOW IT ENDED
Pulled from the market
Roomba, 2002
THE CLAIM
The first to succeed
HOW IT ENDED
It created the category
The Trilobite came first, the Roomba succeeded.
Notes: The Trilobite reached the market a year earlier, in 2001, after a prototype shown on TV in 1996, but it suffered from serious navigation problems and ended up pulled from the market, an unlucky pioneer that arrived before the technology could really make it work. The Roomba, which arrived in September 2002, is more accurately described as the first commercially successful robot vacuum, not the first one overall.

## Slide 7
02
CHAPTER
Three watts of suction
The constraint that redesigned the product

## Slide 8
THE FOCUS GROUP OF SUMMER 2001
200
dollars offered at first: what the product was worth before the test
100
dollars offered after: once they learned it swept without vacuuming
Moms
the real first audience: not the tech enthusiasts the team expected
Notes: The turning point came in the summer of 2001, and it did not come from a lab but from a group of ordinary consumers. The original design of what would become the Roomba was, in practice, a motorized carpet sweeper, it did not actually vacuum. When focus group participants found that out, their willingness to pay collapsed, from 200 dollars to 100. That same session also revealed who the product's first real audience would be, not the tech enthusiasts the team had expected but busy moms managing a household. From there the team went back to the drawing board to add real suction.

## Slide 9
THE POWER BUDGET OF THE FIRST ROOMBA
30 W
the total budget: the energy for the whole robot
3 W
for suction: about 10% of the budget
1,200 W
a conventional vacuum cleaner: the power draw of the time, for comparison
Notes: The most concrete constraint the team had to solve was energy. The robot had a total power budget of 30 W and could only afford to devote about 10% of it, roughly 3 W, to actual suction, versus about 1,200 W for a conventional vacuum cleaner of the time. The fix was not a stronger pump, impossible on that little power, but a suction opening only a couple of millimeters wide, sealed by two rubber vanes that work like a squeegee on hard floors.

## Slide 10
03
CHAPTER
Seeing without eyes
Sensors that add up information

## Slide 11
HOW THE ROBOT WORKS OUT WHAT IS AROUND IT
Ultrasonic ToF
They measure distances
Obstacles in millimeters, any color
Cliff detection
They look down
They spot the top of a staircase
IMU
It measures orientation
It tells if the robot repeats an area
Notes: Ultrasonic time-of-flight sensors measure distance to obstacles in millimeters regardless of surface color, and detect pets or toys. Short-range ones tell floor types apart based on the reflected signal and slow the robot down when it moves from carpet to hardwood. Cliff detection spots drop-offs, like the top of a staircase, to prevent falls. The inertial measurement unit measures roll, pitch and yaw, helping the robot tell whether it is covering the same area twice. There are also pressure sensors, which estimate how full the dustbin is from a drop in airflow, and thermistors, which pause the robot if the motherboard, motors or brushes overheat. Higher-end models add dedicated object-recognition sensors, such as iRobot's PrecisionVision technology, built to spot power cords and shoes, a classic machine learning task.

## Slide 12
04
CHAPTER
From random to a map
Random bounce, LiDAR, vSLAM

## Slide 13
THREE ERAS OF NAVIGATION
Dead reckoning
position estimated blindly
A real map
straight-line paths
Random bounce
until 2010, without a map
LiDAR
Neato XV-11, 2010
vSLAM
cameras, from 2015
Notes: The earliest robots, including the first generations of the Roomba, navigate using random bounce, a set of fairly simple algorithms, spiral, follow the walls, change angle after hitting something, combined with wheel rotation and inertial unit data to blindly estimate where the robot is. The shift came in 2010, when Neato Robotics launched the XV-11, the first consumer model to use LiDAR navigation, a laser that measures distances and lets the robot build an actual map of the space. In 2015 came a second route to the same goal, camera-based mapping, or vSLAM, adopted by both Dyson and iRobot in that year's flagship models. Both share the same weak spot, they struggle in dimly lit spaces and lose effectiveness under a low table or sofa.

## Slide 14
FALSE MYTH
Not every robot moves at random.
Random bounce dominated until 2010. Starting with that year's Neato XV-11, with a laser, and with vSLAM models from 2015, using cameras, the robot builds a map of the room and cleans in straight lines.
Notes: The myth is that robot vacuums just move around at random, bump into furniture and hope for the best. That is only true of the simplest models, the ones without mapping, where the robot spirals, follows walls and changes direction after every bump with no idea where it actually is. Navigation is also the point where the difference between a budget robot and a high-end one becomes most visible.

## Slide 15
WHAT THE MAP SOLVES, AND WHAT IT DOES NOT
With a map
THE PATH
Systematic, straight lines
COVERAGE
It knows where it has been
Physical limits
THE FLOOR
Thick rugs, low furniture
THE BRUSHES
Tangled hair and elastics
Navigation improved, the physics of the floor did not.
Notes: Even the most advanced model remains a device with physical limits that have nothing to do with how sophisticated its navigation is. Thick rugs are still a real obstacle, robots struggle to cross them and often cut power to manage it. Areas under low furniture remain a blind spot even for LiDAR and vSLAM. If someone physically picks up and moves the robot while it is working, it loses track of its position and has to head off in a random direction to reorient itself. And hair or elastic bands tangled in the brushes can overload and overheat the motors, which means periodic manual cleaning is unavoidable.

## Slide 16
THE MARKET IS NO LONGER ONE BRAND
40
million robots, and more: iRobot's official figure from May 2022
2020
China the top market: the world's largest since that year
2025
iRobot's bankruptcy: December 14, then its assets to Picea
Notes: In August 2022 Amazon announced it would acquire iRobot for 1.7 billion dollars, but the deal was blocked by US and European regulators concerned that Amazon could use its e-commerce weight to limit competition. After the deal collapsed, in January 2024, iRobot laid off a third of its staff and suspended research and development, and co-founder and longtime CEO Colin Angle left the company. On December 14, 2025, iRobot filed for bankruptcy, and its assets were taken over by Picea, the Chinese partner that had already been manufacturing its products. Behind this lies a bigger shift, China has been the world's largest market for these robots since 2020, with local companies that, according to IEEE Spectrum, invested two to three times more than iRobot in research and development; iRobot's European market share has fallen to 12%.

## Slide 17
TEST YOURSELF · FOR THE CLASS
Who brought LiDAR to consumer robot vacuums first?
A iRobot's Roomba, in 2002
B Neato Robotics' XV-11, in 2010
C Electrolux's Trilobite, in 1996
Notes: Answer B. The Neato XV-11, launched in 2010, introduced laser mapping, enabling systematic, straight-line navigation in contrast with the random movement, random bounce, of earlier models. If there is time, a second question from the Recap quiz, how much power did the original Roomba devote to suction compared with a conventional vacuum cleaner of the time? (About 3 W, 10% of a 30 W budget, versus roughly 1,200 W for a conventional vacuum cleaner.)

## Slide 18
AND NOW, THE REVIEW
Clear in 30 seconds.
Yours in 10 minutes.
A 5-question quiz and 8 flashcards: recaplica.com/en/technology/robot-vacuum-cleaners/
Sources: IEEE Spectrum · The Robot Report · iRobot · IEC/ASTM 62885-7
Notes: To review, the online Recap has a 5-question quiz and 8 flashcards, with the full list of sources at the bottom of the page.