## Slide 1
TECHNOLOGY · RECAP
Smartphone Battery Life, How to Make It Last Longer
Cycles, heat, and myths worth dropping
Notes: A Recap on how a smartphone battery actually works, what really wears it down, and how to slow the decline — drawing on guidance from Apple, Google, and Battery University.

## Slide 2
THE QUESTION
Why does a phone's battery
feel weaker after two years?
Notes: A battery doesn't fail overnight, it wears down with use: every full charge counts as one cycle, and the capacity it can hold drops a little with each one. The factor that speeds this up most is heat, not age by itself.

## Slide 3
WHAT'S AHEAD
01
How the battery wears down
02
Heat
03
Everyday charging habits
04
The software features that help

## Slide 4
80% CAPACITY IS REACHED AFTER
500
cycles, iPhone 14 and earlier: The threshold Apple states, under ideal conditions.
1000
cycles, iPhone 15: Double the threshold of earlier models.
Notes: These are design figures "under ideal conditions," not guarantees: the source is Apple Support article 101575.

## Slide 5
DEEP DISCHARGE
100% DoD
300 cycles
Draining to nearly zero every time
MEDIUM DISCHARGE
60% DoD
600 cycles
Topping up around the halfway mark
LIGHT DISCHARGE
20% DoD
2,000 cycles
Short, frequent top-ups
Notes: Data from Battery University (BU-808) on NMC chemistry, cycles to 70% remaining capacity (a different threshold from Apple's 80% figure): for the same battery, frequent partial discharges hold up over far more cycles than deep ones. Lithium batteries have no memory effect.

## Slide 6
COLD VERSUS HEAT
Cold
EFFECT
More unexpected shutdowns
LONGEVITY
No known permanent damage
Heat
EFFECT
Capacity lost for good
THRESHOLD
Above 35°C, per Apple
Only heat causes permanent capacity loss
Notes: Apple advises against using or charging a phone above 35°C because it can permanently reduce battery lifespan; cold, by contrast, only raises the risk of unexpected shutdowns when the charge is already low.

## Slide 7
MYTH
You have to run it flat before recharging
Battery University explains that lithium batteries have no memory effect: partial discharges are the norm, while deep discharges close to zero are what actually shortens the cycles available.
Notes: A battery discharged to nearly 100% every time holds up for roughly 300 cycles; discharged to just 20%, it holds up for roughly 2,000, according to Battery University's table (BU-808).

## Slide 8
APPLE, BY DEFAULT
Optimized
80 %
Delays the final stretch of charging
APPLE, IPHONE 15+
Charge Limit
80-100 %
A fixed threshold, your choice
GOOGLE, FROM PIXEL 6A
Limit 80%
80 %
For anyone who ends the day still charged
Notes: Optimized Battery Charging learns your charging routine and delays the finish past 80% until shortly before you usually unplug.

## Slide 9
POP QUIZ
What does the full charge every 10 cycles on Pixel actually do?
A Regenerates the battery chemistry
B Recalibrates the remaining-capacity reading
C Has no real effect
Notes: Answer: it recalibrates the reading, according to Google. Second question for the room: why does heat damage a battery more than cold?

## Slide 10
THE RECAP CONTINUES ONLINE
Clear in 30 seconds.
Yours in 10 minutes.
Read the full Recap, with FAQ and myths recaplica.com/en/technology/smartphone-battery-life-how-to-make-it-last-longer/
Sources: Apple Support · Battery University · Google
Notes: The online Recap also has the quiz, flashcards, and concept map.